## Slide 1: VE370 Mid Review
VE370 TA Group

## Slide 2: Part 1: Context
CPU Performance
Assembly Basic
Convention between Assembly and C
Memory related operations
Addressing
Function Call Convention
Linker

## Slide 3: CPU Performance
CPI, IC, Tc
Pay attention to the unit

## Slide 4: CPU Performance

## Slide 5: Assembly Basic
4 principles:
  Simplicity
  Smaller
  Fast common case
  Compromise (similar formats)
Basic Blocks
How to load 32-bit Constants

## Slide 6: Assembly Basic
R-type, J-type, I-type
Different positions of rs, rt, rd in MIPS vs. machine code

## Slide 7: Assembly to C
Array in C is like

## Slide 8: Assembly to C
f = A[B[g]+1];
g: $s1
B: $s7
A: $s6

## Slide 9: Memory related
lw, lh, lb: sign extended
E.g.
lui $t0, 4096 # get the address 0x1000 0000
lb $s1, 2($t0)

## Slide 10: Memory related
lw, lh, lb: sign extended
E.g.
lui $t0, 4096 # get the address 0x1000 0000
lb $s1, 2($t0) -> 0xFFFF FF89

## Slide 11: Memory Related
Big Endian: Most significant byte stored at least address of a word
(MIPS is Big Endian)
E.g. 0x12345678 in Big endian
In Small endian

## Slide 12: Addressing
Immediate (e.g. addi)
Register (e.g. add)
Base (e.g. lw)
PC-relative (Target address = new PC + offset * 4, new PC = PC +4 )
Pseudodirect (e.g. j and jal)
(on L3 P19)

## Slide 13: Addressing
Address | Code
0x1000 0400 | 000000 00000 01000 01010 00000 101010 (R)
0x1000 0404 | 000101 01010 00000 0000000000000001 (I)
0x1000 0408 | 000010 00000000000000000100000110 (J)
0x1000 040c | 001000 10010 100100000000000000010 (I)
0x1000 0410 | 001001 01000 010000000000000000001 (I)
0x1000 0414 | 000010 00000000000000000100000000 (J)

## Slide 14: Function Call Convention
Before Calling
  change $sp to save $a0~$a3
  Overwrite $a0~$a3
During calling
  Store $ra and any $s0~$s7 that will be used on stack
  Execute and get $v0 $v1
  Restore $s0~$s7
  Restore(pop) frame
After Calling
  Restore $a0~$a3

## Slide 15: Linker
$gp initialized at center of static data
Instructions stored in Text segment (from 0x0040 0000 towards up, won’t exceed 0x1000 0000)
Data stored in Static Data segment (from 0x1000 0000 towards up, won’t exceed 0x1001 0000)

## Slide 16: Linker
A
B

## Slide 17: Linker, Cont’d
100Hex
20Hex

## Slide 18: Linker, Cont’d
100Hex
20Hex
30hex
200hex

## Slide 19: Linker, Cont’d
A
B

## Slide 20: Linker, Cont’d
A
B

## Slide 21: Linker, Cont’d
A
B

## Slide 22: Linker, Cont’d
A
B

## Slide 23: Linker Cont’d
2’s complement
Absolute Address