## Slide 1: VE370 RC8

## Slide 2: Lecture Slides

## Slide 3: Exercise 5.3.5
For a larger direct-mapped cache to have a lower or equal miss rate than a smaller 2-way set associative cache, it would need to have at least double the cache block size. The advantage of such a solution is less misses for near by addresses (spatial locality), but with the disadvantage of suffering longer access times.
To have a lower miss rate on a 2KB 2-way set associative cache:
Eg. 2KB cache, 16-word per block, 2-set
word address: 0, 64, 0, 64, ….
0 and 64 are in the same set.

## Slide 4: Exercise 5.5.2
a.
If L1 miss, send write request to L2.
If L2 hit, write data to L2, set the dirty bit.
If L2 miss, allocate cache block for the missing data, select a replacement victim.
If victim dirty, put it into the write-back buffer, which will be further forwarded into memory.
Issue write miss request to the memory.
Data arrives and is installed in L2 cache.
Write data to L2, set the dirty bit.
Processor resumes execution.

## Slide 5: Exercise 5.5.2
b.
1. If L1 miss, send write request to L2.
2. If L2 hit, write data to L2, set the dirty bit. (go to step 8)
3. If L2 miss, allocate cache block for the missing data, select a replacement victim.
4. If victim dirty, put it into the write-back buffer, which will be further forwarded into memory.
5. Issue write miss request to the memory.
6. Data arrives and is installed in L2 cache.
7. Write data to L2, set the dirty bit.
8. Data arrives and is installed in L1 cache.
9. Processor resumes execution and hits in L1 cache

## Slide 7: Exercise 5.5.5

## Slide 8
With the write back policy, the cache content may be changed and inconsistent with that in the main memory. Thus, upon a read miss, if the replaced block is “dirty”, it will first be written back to the main memory, and then the desired block will be brought into the cache. With write allocation, when a write miss occurs, the corresponding block will be brought to the cache, and then new data will be written into this block. The replaced block, if the dirty bit is set, will need to be written into the main memory first before the write block is brought into the cache. Suppose number of instruction is I, band width W, base CPI=1
a.
Read miss penalty:
Write miss penalty:
Instruction miss penalty:

## Slide 9: Exercise 5.7
5.7.1
P1: 1.51GHz P2: 1.11GHz

## Slide 10: Exercise 5.7.3
5.7.3
first calculate AMAT for P1 &P2
P1: , using clock cycles;
P2 similarly. Answer is 5.1ns, using 5.67 clock cycles.
Second, P1:
P2:

## Slide 11: Exercise 5.7.4-5.7.6
5.7.4
first calculate AMAT for P1 &P2
P1:
Worse
P2:
worse

## Slide 12: Exercise 5.7.4-5.7.6
5.7.5
P1:
P2:

## Slide 13: Exercise 5.7.4-5.7.6
5.7.6
P1 (4.15) is slower than P2 (2.68)
Let r be the miss rate:
AMAT: (ns)
Solve the equation.

## Slide 14: Exercise 5.8.1-5.8.3

## Slide 15
 | Binary address | tag | index | h/m
3 | 11 | 0 | 01 | miss
180 | 10110100 | 10110 | 10 | miss
43 | 101011 | 101 | 01 | miss
2 | 10 | 0 | 01 | hit
191 | 10111111 | 10111 | 11 | miss
88 | 1011000 | 1011 | 00 | miss
190 | 10111110 | 10111 | 11 | hit
14 | 1110 | 1 | 11 | miss
181 | 10110101 | 10110 | 10 | hit
44 | 101100 | 101 | 10 | miss
186 | 10111010 | 10111 | 01 | miss
253 | 11111101 | 11111 | 10 | miss
Index |  |  |  |  |  | 
00 | 88 | 89 |  |  |  | 
01 | 2 | 3 | 42 | 43 | 186 | 187
10 | 180 | 181 | 44 | 45 | 252 | 253
11 | 190 | 191 | 14 | 15 |  | 
bits 7–3 tag, 2–1 index, 0 block offset
The block offset is the address of the desired data within the block.

## Slide 16
 | Binary address | tag | index | h/m
3 | 11 | 11 | N/A | miss
180 | 10110100 | 10110100 | N/A | miss
43 | 101011 | 101011 | N/A | miss
2 | 10 | 10 | N/A | miss
191 | 10111111 | 10111111 | N/A | miss
88 | 1011000 | 1011000 | N/A | miss
190 | 10111110 | 10111110 | N/A | miss
14 | 1110 | 1110 | N/A | miss
181 | 10110101 | 10110101 | N/A | miss
44 | 101100 | 101100 | N/A | miss
186 | 10111010 | 10111010 | N/A | miss
253 | 11111101 | 11111101 | N/A | miss
3181 | 18044 | 43186 | 2253 | 191 | 88 | 190 | 14
 |  |  |  | 191 | 88 | 190 | 14

## Slide 17
 | Binary address | tag | index | h/m
3 | 11 | 11 | N/A | miss
180 | 10110100 | 10110100 | N/A | miss
43 | 101011 | 101011 | N/A | miss
2 | 10 | 10 | N/A | hit
191 | 10111111 | 10111111 | N/A | miss
88 | 1011000 | 1011000 | N/A | miss
190 | 10111110 | 10111110 | N/A | hit
14 | 1110 | 1110 | N/A | miss
181 | 10110101 | 10110101 | N/A | miss
44 | 101100 | 101100 | N/A | miss
186 | 10111010 | 10111010 | N/A | miss
253 | 11111101 | 11111101 | N/A | miss
214186 | 315187 | 18088180252 | 18189181253 | 4214 | 4315 | 19044 | 19145
LRU

## Slide 18
 | Binary address | tag | index | h/m
3 | 11 | 11 | N/A | miss
180 | 10110100 | 10110100 | N/A | miss
43 | 101011 | 101011 | N/A | miss
2 | 10 | 10 | N/A | hit
191 | 10111111 | 10111111 | N/A | miss
88 | 1011000 | 1011000 | N/A | miss
190 | 10111110 | 10111110 | N/A | miss
14 | 1110 | 1110 | N/A | miss
181 | 10110101 | 10110101 | N/A | hit
44 | 101100 | 101100 | N/A | miss
186 | 10111010 | 10111010 | N/A | miss
253 | 11111101 | 11111101 | N/A | miss
2 | 3 | 18044186253 | 18145187253 | 42 | 43 | 1908819014 | 1918919115
2 | 3 |  |  | 42 | 43 |  | 
MRU
The best miss rate is

## Slide 19: Exercise 5.8.4

## Slide 20
Base CPI: 1.5
Memory miss cycles: =
Total CPI
Total CPI:
Total CPI: